ND series

Inline planetary gearboxes

## Model: NDxxx - xx - Sx - Px / Motor model

| NDxxx | Series and Nominal size | ND40, ND60, ND90, ND120, ND160 |
| --- | --- | --- |
| xx | Ratio | L1 (1 stage): 4, 5, 7, 10 L2 (2 stages): 16, 20, 25, 35, 40, 50, 70, 100 L3 (3 Stages): 64, 80, 100, 125, 140, 175, 245, 280, 350, 400, 500, 700, 1000 |
| Sx | Output shaft | S1: smooth shaft without slot. S2: smooth shaft with slot. |
| Px | Backlash | P1: Precise backlash. P2: Standard backlash. |
| Motor model (Optional) | The motor's model that you use to work with this gearboxes. |

For example, ND90-10-S1-P2 means ND series gearboxes, nominal size 90, Ratio 10, Smooth shaft without slot, Standard backlash.

Gearboxes Properties and Features

|  | Stages | Ratio | ND40 | ND60 | ND90 | ND120 | ND160 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Rated Output Torque (Nm) | L1 | 4 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 5 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 7 | 6.6 | 33 | 92 | 168 | 378 |
|  |  | 10 | 4.8 | 15 | 54 | 85 | 310 |
|  | L2 | 16 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 20 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 25 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 35 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 40 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 50 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 70 | 6.6 | 33 | 92 | 168 | 378 |
|  |  | 100 | 4.8 | 15 | 54 | 85 | 310 |
|  | L3 | 64 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 80 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 100 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 125 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 140 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 175 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 245 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 280 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 350 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 400 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 500 | 12.2 | 42 | 112 | 210 | 585 |
|  |  | 700 | 6.6 | 33 | 92 | 168 | 378 |
|  |  | 1000 | 4.8 | 15 | 54 | 85 | 310 |
| Max. Output Torque (Nm) | L1-L3 | 4-1000 | 2 x Rated output torque |
| Rated input speed (rpm) | L1-L3 | 4-1000 | 4000 | 4000 | 4000 | 4000 | 3000 |
| Max. input speed (rpm) | L1-L3 | 4-1000 | 6000 | 6000 | 6000 | 6000 | 5000 |
| Rated radial load (N) | L1-L3 | 4-1000 | 300 | 680 | 1750 | 3100 | 6550 |
| Rated axial load (N) | L1-L3 | 4-1000 | 150 | 340 | 875 | 1550 | 3275 |
| Moment of inertia (kg.cm^2) | L1 | 4, 5 | 0.15 | 0.48 | 1.75 | 12.8 | 22.4 |
|  |  | 7-10 | 0.15 | 0.42 | 1.45 | 11.4 | 18.8 |
|  | L2 | 15-40 | 0.15 | 0.45 | 1.52 | 12.2 | 18.6 |
|  |  | 50-100 | 0.15 | 0.32 | 1.35 | 11.5 | 16.9 |
|  | L3 | 64-280 | 0.15 | 0.32 | 1.36 | 12.2 | 16.3 |
|  |  | 350-1000 | 0.15 | 0.32 | 1.29 | 12.2 | 16.3 |
| Lifetime (hrs) | L1-L3 | 4-1000 | 20000 |
| Efficiency (%) | L1 | 4-10 | 97% | 97% | 97% | 97% | 97% |
|  | L2 | 16-100 | 94% | 94% | 94% | 94% | 94% |
|  | L3 | 64-1000 | 91% | 91% | 91% | 91% | 91% |
| Weight (kg) | L1 | 4-10 | 0.7 | 1.4 | 3 | 7.2 | 21 |
|  | L2 | 16-100 | 0.9 | 1.6 | 3.5 | 9.2 | 26 |
|  | L3 | 64-1000 | 1.2 | 1.8 | 4 | 11.5 | 31 |
| Noise (dB) | L1-L3 | 4-1000 | ≤65 | ≤65 | ≤68 | ≤68 | ≤72 |
| Ambient temp. | L1-L3 | 3-1000 | -20 to 90 °C, -4 to 194 °F |
| Precision backlash (Arcmin) | L1 | 4-10 | ≤5 | ≤5 | ≤5 | ≤5 | ≤5 |
|  | L2 | 16-100 | ≤7 | ≤7 | ≤7 | ≤7 | ≤7 |
|  | L3 | 64-1000 | ≤9 | ≤9 | ≤9 | ≤9 | ≤9 |
| Standard backlash (Arcmin) | L1 | 4-10 | ≤10 | ≤10 | ≤10 | ≤10 | ≤10 |
|  | L2 | 16-100 | ≤12 | ≤12 | ≤12 | ≤12 | ≤12 |
|  | L3 | 64-1000 | ≤15 | ≤15 | ≤15 | ≤15 | ≤15 |

|  | ND40 | ND60 | ND90 | ND120 | ND160 |
| --- | --- | --- | --- | --- | --- |
| Stages | 1-2-3 | 1-2-3 | 1-2-3 | 1-2-3 | 1-2-3 |
| D1 | Φ67 | Φ79 | Φ109 | Φ135 | Φ168 |
| D2 | 8- Φ3.4 | 8-Φ4.5 | 8- Φ5.5 | 8- Φ5.5 | 12- Φ6.6 |
| D3 | Φ20 | Φ31.5 | Φ50 | Φ63 | Φ80 |
| D4 | 4-M3X5 | 7-M5X7 | 7-M6X10 | 11-M6X12 | 1-M8X15 |
| D5 | Φ3X5 | Φ5X6 | Φ6X7 | Φ6X7 | Φ8X10 |
| D6 | Φ12X4 | Φ20X4 | Φ31.5X12 | Φ40X12 | Φ50X12 |
| D7 | Φ28 | Φ40 | Φ63 | Φ78 | Φ100 |
| D8 | Φ47 | Φ64 | Φ90 | Φ110 | Φ140 |
| D9 | Φ72 | Φ86 | Φ118 | Φ145 | Φ179 |
| L1 | 3 | 3 | 6 | 6 | 6 |
| L2 | 7 | 7 | 10 | 10 | 14.5 |
| L3 | 17.5 | 19.5 | 30 | 29 | 38 |
| L4 | 4 | 5 | 8 | 10 | 12 |
| L5 | 93-108-121.5 | 104-120-136 | 136-157-178 | 165-194-222 | 215-267-316 |
| C1* | 466370 | 707585 | 100115145 | 145165 | 200215 |
| C2* | M4*P0.7 M5*P0.8 | M5*P0.8 M6*P1.0 | M6*P1.0 M8*P1.25 | M8*P1.25 M10*P1.5 | M10*P1.5 M12*P1.75 |
| C3* | 6811 | 11141619 | 16192224 | 19222428 | 22242835 |
| C4* | 26 | 35 | 40 | 50 | 60 |
| C5* | 30,40,50 | 50,60,70 | 80,95,110 | 110130 | 114.3,130,180 |
| C6* | 3.5 | 4 | 4 | 5 | 6 |
| C7* | 42,62 | 62,92 | 92110130 | 130150 | 175180 |

* C1 thru C7 is common interface to motors. If you have special requirement, please call us for customizing.