NE series

Inline planetary gearboxes

Model: NExxx - xx - Sx - Px / Motor model

| NExxx | Series and Nominal size | NE40, NE60, NE90, NE120, NE160, NE200 |
| --- | --- | --- |
| xx | Ratio | L1 (1 stage): 4, 5, 7, 10 L2 (2 stages): 16, 20, 25, 35, 40, 50, 70, 100 L3 (3 Stages): 64, 80, 100, 125, 140, 175, 245, 280, 350, 400, 500, 700, 1000 |
| Sx | Output shaft | S1: smooth shaft without slot. S2: smooth shaft with slot. |
| Px | Backlash | P1: Precise backlash. P2: Standard backlash. |
| Motor model (Optional) | The motor's model that you use to work with this gearboxes. |

For example, NE90-10-S1-P2 means NE series gearboxes, nominal size 90, Ratio 10, Smooth shaft without slot, Standard backlash.

Gearboxes Properties and Features

|  | Stages | Ratio | NE40 | NE60 | NE90 | NE120 | NE160 | NE200 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rated Output Torque (Nm) | L1 |  |  |  |  |  |  |  |
|  |  | 4 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 5 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 7 | 6.6 | 33 | 92 | 168 | 378 | 850 |
|  |  | 10 | 4.8 | 15 | 54 | 85 | 310 | 630 |
|  | L2 | 16 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 20 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 25 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 35 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 40 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 50 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 70 | 6.6 | 33 | 92 | 168 | 378 | 850 |
|  |  | 100 | 4.8 | 15 | 54 | 85 | 310 | 630 |
|  |  | 64 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 80 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  | L3 | 100 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 125 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 140 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 175 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 245 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 280 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 350 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 400 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 500 | 12.2 | 42 | 112 | 210 | 585 | 1140 |
|  |  | 700 | 6.6 | 33 | 92 | 168 | 378 | 850 |
|  |  | 1000 | 4.8 | 15 | 54 | 85 | 310 | 630 |
| Max. Output Torque (Nm) | L1-L3 | 4-1000 | 2 x Rated output torque |
| Rated input speed (rpm) | L1-L3 | 4-1000 | 4000 | 4000 | 4000 | 4000 | 3000 | 2500 |
| Max. input speed (rpm) | L1-L3 | 4-1000 | 6000 | 6000 | 6000 | 6000 | 5000 | 4000 |
| Rated radial load (N) | L1-L3 | 4-1000 | 300 | 680 | 1750 | 3100 | 6550 | 12400 |
| Rated axial load (N) | L1-L3 | 4-1000 | 150 | 340 | 875 | 1550 | 3275 | 6200 |
| Moment of inertia (kg.cm^2) | L1 | 4-5 | 0.15 | 0.48 | 1.75 | 12.8 | 22.4 | 45.3 |
|  |  | 7-10 | 0.15 | 0.42 | 1.45 | 11.4 | 18.6 | 44.8 |
|  | L2 | 15-40 | 0.15 | 0.45 | 1.52 | 12.2 | 18.6 | 45.2 |
|  |  | 50-100 | 0.15 | 0.32 | 1.35 | 11.5 | 16.9 | 44.6 |
|  | L3 | 64-280 | 0.15 | 0.32 | 1.36 | 12.2 | 16.3 | 44.2 |
|  |  | 350-1000 | 0.15 | 0.32 | 1.29 | 12.2 | 16.3 | 42.6 |
| Lifetime (hrs) | L1-L3 | 3-1000 | 20000 |
| Efficiency (%) | L1 | 4-10 | 97% | 97% | 97% | 97% | 97% | 97% |
|  | L2 | 16-100 | 94% | 94% | 94% | 94% | 94% | 94% |
|  | L3 | 64-1000 | 91% | 91% | 91% | 91% | 91% | 91% |
| Weight (kg) | L1 | 4-10 | 0.6 | 1 | 3 | 6.2 | 19 | 42 |
|  | L2 | 16-100 | 0.9 | 1.5 | 4 | 8 | 24 | 50 |
|  | L3 | 64-1000 | 1.2 | 2 | 5 | 9.8 | 29 | 58 |
| Noise (dB) | L1-L3 | 4-1000 | ≤65 | ≤65 | ≤68 | ≤68 | ≤72 | ≤72 |
| Ambient temp. | L1-L3 | 4-1000 | -20 to 90 °C, -4 to 194 °F |
| Precision backlash (arcmin) | L1 | 4-10 | ≤5 | ≤5 | ≤5 | ≤5 | ≤5 | ≤5 |
|  | L2 | 16-100 | ≤7 | ≤7 | ≤7 | ≤7 | ≤7 | ≤7 |
|  | L3 | 64-1000 | ≤9 | ≤9 | ≤9 | ≤9 | ≤9 | ≤9 |
| Standard backlash (arcmin) | L1 | 4-10 | ≤10 | ≤10 | ≤10 | ≤10 | ≤10 | ≤10 |
|  | L2 | 16-100 | ≤12 | ≤12 | ≤12 | ≤12 | ≤12 | ≤12 |
|  | L3 | 64-1000 | ≤15 | ≤15 | ≤15 | ≤15 | ≤15 | ≤15 |

|  | NE40 | NE60 | NE90 | NE120 | NE160 | NE200 |
| --- | --- | --- | --- | --- | --- | --- |
| Stages | 1-2-3 | 1-2-3 | 1-2-3 | 1-2-3 | 1-2-3 | 1-2-3 |
| D1 | 34 | 52 | 70 | 100 | 145 | 170 |
| D2 | M4x9 | M5x10 | M6x12 | M10X18 | M12X18 | M12X18 |
| D3 | 10 | 14 | 20 | 25 | 40 | 55 |
| D4 | 26 | 40 | 60 | 80 | 130 | 145 |
| D5 | 15 | 17 | 25 | 35 | 55 | 70 |
| D6 | M3*P0.7 | M5*P0.8 | M6*P1.25 | M10*P1.75 | M12*P2.0 | M16*P2.5 |
| L1 | 40 | 60 | 90 | 120 | 160 | 200 |
| L2 | 26 | 37 | 46 | 58 | 92 | 100 |
| L3 | 3 | 5 | 6 | 8 | 10 | 12 |
| L4 | 20 | 30 | 38 | 50 | 80 | 85 |
| L5 | 16 | 24 | 32 | 40 | 70 | 75 |
| L6 | 2 | 3 | 3 | 5 | 5 | 6 |
| C1* | 46,63,70 | 70,75,85 | 100,115,145 | 145,165 | 200,215 | 200,215,265 |
| C2* | M4*P0.7 M5*P0.8 | M5*P0.8 M6*P1.0 | M6*P1.0 M8*P1.25 | M8*P1.25 M10*P1.5 | M10*P1.5 M12*P1.75 | M12*P1.75 M16*P2.0 |
| C3* | 6,8,11 | 11,14,16 | 16,19,22 | 19,22,24,28 | 22,24,28,35 | 35,38,42,48 |
| C4* | 26 | 35 | 40 | 50 | 60 | 80 |
| C5* | 30,40,50 | 50,60,70 | 80,95,110 | 110,130 | 114,180 | 180,230 |
| C6* | 3.5 | 4 | 4 | 5 | 6 | 6 |
| C7* | 42,62 | 62,92 | 92,110,130 | 130,150 | 150,190 | 190,240 |
| C8* | 8 | 11 | 16 | 18.5 | 22 | 25 |
| C9* | 88-108-128 | 120-146-166 | 155-180-205 | 194-226-257 | 280-334-388 | 350-410-470 |
| B1 | 3 | 5 | 6 | 8 | 12 | 16 |
| H1 | 11.2 | 16 | 22.5 | 28 | 43 | 59 |

* C1 thru C9 is common interface to motors. If you have special requirement, please call us for customizing.